SparkFun TMP102 Temperature Sensor

We use the SparkFun TMP102 Temperature Sensor.

SparkFun provides a Hookup Guide for the SparkFun TMP102 Temperature Sensor.
# Arduino IDE
We use the SparkFun TMP102 Breakout Library.

Open Arduino IDE
$: sudo arduino
> Select Sketch>Include Library>Manage Libraries…
> Select SparkFun TMP102 Breakout
> Click 1.1.0 Install
$: sudo chmod -R +666 /opt/SparkFun_RedBoard_Turbo

An already downloaded copy of the SparkFun TMP102 library (used by installation script and Dockerfile) can be found here:
sw/SparkFun_RedBoard_Turbo/SparkFun_TMP102_Temperature_Sensor/SparkFun_TMP102_Arduino_Library-master.zip

The library is installed under
/opt/SparkFun_RedBoard_Turbo/Arduino/libraries/SparkFun_TMP102_Breakout.
# Read Temperature
We communicate with the SparkFun TMP102 Temperature Sensor over I2C using address 0x48.

Read Temperature

$: sudo cp -r sw/SparkFun_RedBoard_Turbo/SparkFun_TMP102_Temperature_Sensor/read_temperature /opt/SparkFun_RedBoard_Turbo/Arduino
$: sudo chmod -R +666 /opt/SparkFun_RedBoard_Turbo

Arduino IDE
$: arduino
> File>Sketchbook>read_temperature
> Click Serial Monitor icon
> Select 115200 baud
> Click Upload icon (until flash is successful)

SparkFun TMP102 Temperature Sensor
Temperature [C]: 29.44
# Script
Run as part of the Sensor Suite installation script
sw/NVIDIA_Jetson_Xavier_NX/Scripts$ bash install-7-Sensor_Suite.sh
# Dockerfile
Part of the Sensor Suite Dockerfile
sw/NVIDIA_Jetson_Xavier_NX/Docker/Dockerfile-7-Sensor_Suite