SparkFun ICM20948 IMU

We use the SparkFun ICM-20948 9DoF IMU as our Body Frame IMU.

SparkFun provides a Hookup Guide for the SparkFun ICM20948 9DoF IMU.

# Arduino IDE
We use the SparkFun ICM20948 Library.

Open Arduino IDE
$: sudo arduino
> Select Sketch>Include Library>Manage Libraries…
> Select Sparkfun 9DoF IMU Breakout – IMC 20948 – Arduino Library
> Click 1.2.5 Install
$: sudo chmod -R +666 /opt/SparkFun_RedBoard_Turbo

An already downloaded copy of the SparkFun ICM20948 library (used by installation script and Dockerfile) can be found here:
sw/SparkFun_RedBoard_Turbo/SparkFun_ICM20948_IMU/SparkFun_ICM-20948_ArduinoLibrary-master.zip

The library is installed under
/opt/SparkFun_RedBoard_Turbo/Arduino/libraries/SparkFun_9DoF_IMU_Breakout_-_ICM_20948_-_Arduino_Library.

# Read IMU
We communicate with the SparkFun ICM20948 IMU over I2C using address 0x69.

Read IMU
$: sudo cp -r sw/SparkFun_RedBoard_Turbo/SparkFun_ICM20948_IMU/read_imu /opt/SparkFun_RedBoard_Turbo/Arduino
$: sudo chmod -R +666 /opt/SparkFun_RedBoard_Turbo

Arduino IDE
$: arduino
> File>Sketchbook>read_imu
> Click Serial Monitor icon
> Select 115200 baud
> Click Upload icon (until flash is successful)

SparkFun ICM20948 IMU
Linear Acceleration [mg]: -6.35/48.83/1022.95, Angular Rate [dps]: 1.69/-2.73/0.75, Magnetic Field [uT]: 5.70/14.55/15.90, Temperature [C]: 29.47
# Script
Run as part of the Sensor Suite installation script
sw/NVIDIA_Jetson_Xavier_NX/Scripts$ bash install-7-Sensor_Suite.sh
# Dockerfile
Part of the Sensor Suite Dockerfile
sw/NVIDIA_Jetson_Xavier_NX/Docker/Dockerfile-7-Sensor_Suite