SparkFun LSM9DS1 IMU

We use two (2) SparkFun LSM9DS1 IMUs, each is fixed to one of the two (2) Arducam Sony IMX219 camera modules.

SparkFun provides a Hookup Guide for the SparkFun LSM9DS1 IMU.

# Arduino IDE
We use the SparkFun LSM9DS1 Library.

Open Arduino IDE
$: sudo arduino
> Select Sketch>Include Library>Manage Libraries…
> Select Sparkfun LSM9DS1 IMU
> Click 2.0.0 Install
$: sudo chmod -R +666 /opt/SparkFun_RedBoard_Turbo

An already downloaded copy of the SparkFun LSM9DS1 library (used by installation script and Dockerfile) can be found here:
sw/SparkFun_RedBoard_Turbo/SparkFun_LSM9DS1_IMU/SparkFun_LSM9DS1_Arduino_Library-master.zip

The library is installed under
/opt/SparkFun_RedBoard_Turbo/Arduino/libraries/SparkFun_LSM9DS1_IMU.

# Read IMU
We communicate with the SparkFun LSM9DS1 IMUs over I2C, with the left one (seen from the inside) using the default addresses 0x6B (acc/gyr) and 0x1E (mag) and the right one using the alternative addresses 0x6A and 0x1C.

Read IMU

$: sudo cp -r sw/SparkFun_RedBoard_Turbo/SparkFun_LSM9DS1_IMU/read_imu_camera /opt/SparkFun_RedBoard_Turbo/Arduino
$: sudo chmod -R +666 /opt/SparkFun_RedBoard_Turbo

Arduino IDE
$: arduino
> File>Sketchbook>read_imu_camera
> Click Serial Monitor icon
> Select 115200 baud
> Click Upload icon (until flash is successful)

> Change I2C address to alternative addresses in read_imu_camera.ino: imu.begin(0x6A, 0x1C)
> Click Upload icon (until flash is successful)

SparkFun LSM9DS1 IMU
Linear Acceleration [g]: 0.01/-1.01/-0.10, Angular Rate [dps]: 0.01/1.66/-2.13, Magnetic Field [gauss]: -0.68/1.34/0.19
# Script
Run as part of the Sensor Suite installation script
sw/NVIDIA_Jetson_Xavier_NX/Scripts$ bash install-7-Sensor_Suite.sh
# Dockerfile
Part of the Sensor Suite Dockerfile
sw/NVIDIA_Jetson_Xavier_NX/Docker/Dockerfile-7-Sensor_Suite