SparkFun LPS25HB Pressure Sensor

We use the SparkFun LPS25HB Pressure Sensor.
# Arduino IDE
We use the SparkFun LPS25HB Library.

Open Arduino IDE
$: sudo arduino
> Select Sketch>Include Library>Manage Libraries…
> Select SparkFun LPS25HB Pressure Sensor Library
> Click 1.1.0 Install
$: sudo chmod -R +666 /opt/SparkFun_RedBoard_Turbo

An already downloaded copy of the SparkFun LPS25HB library (used by installation script and Dockerfile) can be found here:
sw/SparkFun_RedBoard_Turbo/SparkFun_LPS25HB_Pressure_Sensor/SparkFun_LPS25HB_Arduino_Library-master.zip

The library is installed under
/opt/SparkFun_RedBoard_Turbo/Arduino/libraries/SparkFun_LPS25HB_Pressure_Sensor_Library.
# Read Pressure (air)
We communicate with the SparkFun LPS25HB Pressure Sensor over I2C using address 0x5D.

Read Pressure
$: sudo cp -r sw/SparkFun_RedBoard_Turbo/SparkFun_LPS25HB_Pressure_Sensor/read_pressure /opt/SparkFun_RedBoard_Turbo/Arduino
$: sudo chmod -R +666 /opt/SparkFun_RedBoard_Turbo

Arduino IDE
$: arduino
> File>Sketchbook>read_pressure
> Click Serial Monitor icon
> Select 115200 baud
> Click Upload icon (until flash is successful)

SparkFun LPS25HB Pressure Sensor
Pressure [hPa]: 1010.65, Temperature [C]: 28.09

# Script
Run as part of the Sensor Suite installation script
sw/NVIDIA_Jetson_Xavier_NX/Scripts$ bash install-7-Sensor_Suite.sh
# Dockerfile
Part of the Sensor Suite Dockerfile
sw/NVIDIA_Jetson_Xavier_NX/Docker/Dockerfile-7-Sensor_Suite