SparkFun NEO-M9N GPS

We use the SparkFun NEO-M9N GPS as our GNSS receiver. The NEO-M9N GNSS module is manufactured by u-box.

u-blox published a comprehensive guide GPS Essentials of Satellite Navigation Compendium for a good foundation on how Satellite Navigation works. u-blox provides u-center, a free software tool under Windows (user guide), for interfacing to and configuring their GNSS receivers. u-blox provides an integration manual for a detailed description of their GNSS receiver. u-blox provides a detailed interface document for interfacing with their GNSS receiver, including NMEA, RTCM and u-blox’s proprietary UBX binary interface.

SparkFun provides a Hookup Guide for the SparkFun NEO-M9N GPS.

# u-blox Firmware
u-blox provides u-center, a free software tool under Windows (user guide), to update the firmware on the GNSS module.

SparkFun provides tutorials on Getting Started with U-Center for u-blox and how to upgrade firmware of a u-blox GNSS receiver.

U-center requires the use of a Windows computer. Connect a USB to USB-C cable from the Windows computer to the USB-C port of the SparkFun NEO-M9N GPS.

Installation u-center on the Windows computer
Firefox: https://www.u-blox.com/en/product/u-center
> Click on u-center for Windows v.21.05
> Save
~/Downloads/u-center_v21.05.exe
> Double-click u-center_v21.05.exe
> Double-click u-center_v21.05

Check firmware version
> Launch u-center
> Select Receiver>Connection> COM <x>
Receiver Port <> icon turns green
> Select View>Messages View
> Select UBX>MON (Monitor)>VER (Version)
FWVER=SPG 4.0.3

Download firmware
Firefox: https://www.u-blox.com/en/product/neo-m9n-module
> Click Documentation & resources
> Click M9 SPG 4.0.4 firmware Link Download
> Save File
~/Downloads/JU_EXT_404…..bin

Upgrade firmware
> Launch u-center
> Select Receiver>Connection> COM <x>
Receiver Port <> icon turns green
> Select Tools>Firmware Update ...
> Enter Firmware image: ~/Downloads/JU_EXT_404…..bin
> Click GO (bottom left)
Firmware Update Success

# Arduino IDE
We use the SparkFun u-blox GNSS Arduino Library.

Open Arduino IDE
$: sudo arduino
> Select Sketch>Include Library>Manage Libraries…
> Select SparkFun u-blox GNSS Arduino Libray
> Click 2.0.7 Install
$: sudo chmod -R +666 /opt/SparkFun_RedBoard_Turbo

An already downloaded copy of the SparkFun u-blox GNSS library (used by installation script and Dockerfile) can be found here:
sw/SparkFun_RedBoard_Turbo/SparkFun_NEO-M9N_GPS/SparkFun_u-blox_GNSS_Arduino_Library-master.zip

The library is installed under
/opt/SparkFun_RedBoard_Turbo/Arduino/libraries/SparkFun_u-blox_GNSS_Arduino_Library.

# Read GNSS
We communicate with the SparkFun NEO-M9N GPS over I2C using address 0x42.

Read GNSS

$: sudo cp -r sw/SparkFun_RedBoard_Turbo/SparkFun_NEO-M9N_GPS/read_gnss /opt/SparkFun_RedBoard_Turbo/Arduino
$: sudo chmod -R +666 /opt/SparkFun_RedBoard_Turbo

Arduino IDE
$: arduino
> File>Sketchbook>read_gnss
> Click Serial Monitor icon
> Select 115200 baud
> Click Upload icon (until flash is successful)

SparkFun NEO-M9N GPS
Current update rate: 1
Lat [degrees]: 32.96 Long [degrees]: -117.23 Alt [m]: 46.78 AltMSL [m]: 80.41 Fix: 3D Speed [m/s]: 0.86 Heading [degrees]: 281 pDOP: 3.18 SIV: 5 2021-6-21 1:16:44 Time is valid Date is valid
# Script
Run as part of the Sensor Suite installation script
sw/NVIDIA_Jetson_Xavier_NX/Scripts$ bash install-7-Sensor_Suite.sh
# Dockerfile
Part of the Sensor Suite Dockerfile
sw/NVIDIA_Jetson_Xavier_NX/Docker/Dockerfile-7-Sensor_Suite