Zio INA219 Current and Voltage Sensor

We use the Zio INA219 Current and Voltage Sensor purchased through SparkFun.

Smart Prototyping provides a Start Guide for the Zio Current and Voltage Sensor.

# Arduino IDE
We use Adafruit’s INA219 Library and BUS IO Library.

Open Arduino IDE
$: sudo arduino
> Select Sketch>Include Library>Manage Libraries…
> Select Adafruit INA219
> Click 1.1.0 Install
> Click Install Adafruit INA219 only
> Select Sketch>Include Library>Manage Libraries…
> Select Adafruit Bus IO
> Click 1.7.3 Install
$: sudo chmod -R +666 /opt/SparkFun_RedBoard_Turbo

Already downloaded copies of the Adafruit INA219 and BUS IO libraries (used by installation script and Dockerfile) can be found here:
sw/SparkFun_RedBoard_Turbo/Zio_INA219_Current_and_Voltage_Sensor/Adafruit_INA219-master.zip and Adafruit_BusIO-master.zip

The libraries are installed under
/opt/SparkFun_RedBoard_Turbo/Arduino/libraries/Adafruit_INA219 and Adafruit_BusIO.

# Read Power
We communicate with the Zio INA Current and Voltage Sensor over I2C using address 0x40.

Read Power

$: sudo cp -r sw/SparkFun_RedBoard_Turbo/Zio_INA219_Current_and_Voltage_Sensor/read_power /opt/SparkFun_RedBoard_Turbo/Arduino
$: sudo chmod -R +666 /opt/SparkFun_RedBoard_Turbo

Arduino IDE
$: arduino
> File>Sketchbook>read_power
> Click Serial Monitor icon
> Select 115200 baud
> Click Upload icon (until flash is successful)

Zio INA219 Current and Voltage Sensor
Bus Voltage [V]: 19.93 Shunt Voltage [mV]: 62.64 Load Voltage [V]: 19.99 Current [mA]: 596.30 Power [mW]: 11878
# Script
Run as part of the Sensor Suite installation script
sw/NVIDIA_Jetson_Xavier_NX/Scripts$ bash install-7-Sensor_Suite.sh
# Dockerfile
Part of the Sensor Suite Dockerfile
sw/NVIDIA_Jetson_Xavier_NX/Docker/Dockerfile-7-Sensor_Suite